## Slide 1
Coordenadores: Paulo Artaxo e Maria Assunção F. Silva Dias, Universidade de São Paulo
Equipe: Henrique Barbosa (IFUSP), Joel Ferreira de Brito (IFUSP), Luciana Rizzo (UNIFESP-Diadema), Theotônio Pauliquevis (UNIFESP-Diadema), Karla Longo (INPE), Saulo Freitas (INPE), David Adams (UEA), Rodrigo Souza (UEA), Wanderley Bastos (UNIR-Porto Velho), Sandra Hacon (FIOCRUZ), Fernando Morais (IFUSP), Alcides Ribeiro (IFUSP), Ana Loureiro (IFUSP), Fábio Jorge (IFUSP), Lívia Oliveira (INPA), Joiada Silva (UNIR-Porto Velho), Rodrigo Marques (UFMT) e José Nogueira (UFMT) , Scot Martin (Harvard), Meinrat Andreae (Max Planck) e muitos outros.
Conferência CONCLIMA 12 de Setembro de 2013
Projeto Temático FAPESP 2008/58100-2
AEROCLIMA - Efeitos diretos e indiretos de aerossóis no clima da Amazônia e Pantanal

## Slide 2
Susceptibility and expected reaction to stresses of global climate change as well as pollution introduced by future regional economic development are not known or quantified at present time.
Source: Barth et al., “Coupling between Land Ecosystems and the Atmospheric Hydrologic Cycle through Biogenic Aerosol Particles,” BAMS, 86, 1738-1742, 2005.
Amazon Basin has strong coupling between terrestrial ecosystem and the hydrologic cycle: The linkages among carbon cycle, aerosol life cycle, and cloud life cycle need to be understood and quantified.

## Slide 3
Amazonia: 3 different types of aerosols
Biogenic (primary and SOA)
Biomass Burning
Dust from Sahara
Each with VERY different properties and impacts

## Slide 4
Aerosol Cycling in Amazonia

## Slide 5
Aerosols, radiation, clouds and greenhouse gases in the global climate system
The major uncertainties in the climate system

## Slide 6
Aerosol and cloud lifecycles

## Slide 7
Pöschl et al., “Rainforest aerosols as biogenic nuclei of clouds and precipitation in the Amazon,” Science, 2010, 329, 1513-1516.
Particle-Limited Regime
Anthropogenically affected continents
Amazon
Basin
Amazon Basin:
Low aerosol number concentrations +
High water vapor concentration =
Especially susceptible.
Possibility of large changes in energy flows and rainfall patterns
High sensitivity to Pollution in Pristine Regions

## Slide 8
Chart: Deforestation in Amazonia 1977-2012 in km² per year
| 77/88* | 88/89 | 89/90 | 90/91 | 91/92 | 92/93 | 92/94 | 94/95 | 95/96 | 96/97 | 97/98 | 98/99 | 99/00 | 00/01 | 01/02 | 02/03 | 03/04 | 04/05 | 05/06 | 06/07 | 07/08 | 08/09 | 09/10 | 10/11 | 11/12
 | 21050 | 17770 | 13730 | 11130 | 13786 | 14896 | 14896 | 29059 | 18161 | 13227 | 17383 | 17259 | 18226 | 18165 | 21651 | 25396 | 27771 | 19014 | 14286 | 11651 | 12911 | 7464 | 7000 | 6418 | 4571
What public policies are needed to sustain this reduction?
Deforestation was reduced from 27,700 Km² in 2004 to 4,571 Km² in 2012.
A very dynamical system, and we need to know what effects on the ecosystem these changes have produced
4.571 Km² in 2012

## Slide 9
Yearly deforestation over the Brazilian Amazon region (INPE, 2010) compared to MODIS daily smoke optical depth and the daily number of hot pixels from NOAA-12 and NOAA-15. The results are shown according to the hydrological year, from August 1st of the previous year to July 31st of the years shown in the graph. The vertical lines indicate August 1st , which correspond to the onset of the burning season.
Yearly deforestation and MODIS AOD and hot pixels from NOAA-12/15

## Slide 10
AOD 550 nm 1999-2012 in Porto Velho, Rondonia

## Slide 11: Aerosol composition in wet-season Amazonia
Fine Fraction
1.7 µg m-3
Coarse Fraction
5.7 µg m-3
Martin et al., 2010

## Slide 12
Biological Particles & Molecules

## Slide 13
  POLLEN/SPORE Dp DAY NIGHT
  (m) (m-3) (m-3)
  Fungal spores:
  Alternaria longissima 12-60 190 10
  Ascospores 2-22 2,064 7,416
  Aspergillus/
  Penicillium 2-6 2,470 0
  Basidiospores 12 95 5
  Cladosporium 2-12 3,040 3,090
  Dreschlera/
  Exserohium 10-70 152 412
  Myxomycete 8 10 2,060
  Other 5-350 1,348 1,462
  Periconia 10 57 309
  Powdery Mildew 7-13 76 1,648
  Rust 8-12 1,710 3,605
  Smut 5-7 10 9,167
  Yeast 2-10 12,255 203,528
  TOTAL FUNGAL 23,462 234,154
  Algae (unknown type) 8 20 0
  TOTAL ALGAE 20 0
Fungal hyphae
Fungal spores
Brochosomes
Trichome
(leaf fragment)
Fungal spore
Pollen
Fern spore
Fungal spore
Natural biogenic particles
Source: MPIC, Mainz
10 times higher at night !!!

## Slide 14
Manaus
Rbio Cuieiras
Dry aerosol (RH<40%)
Site continuously operational since Feb 2008.
Manaus and Porto Velho
Long term monitoring stations in Amazonia

## Slide 15
-25
5
-5
-15
-25
-80
-70
-60
-50
-40
-30
-15
-80
-70
-60
-50
-61
-62
-63
-64
-10
-11
-12
-40
-30
Porto Velho
Porto Velho aerosol and trace gases sampling location

## Slide 16
Centro de Pesquisas do Pantanal (CPP-SESC), Universidade Federal do Mato Grosso

## Slide 17
Four flux towers with 85 meters already in operation at the ATTO site
Measurements at 6 levels for
Ozone, CO, VOCs (PTR-MS), aerosol number size distribution, composition with ACSM, Light scattering (TSI Neph), light absorption using MAAP, Aethalometer, SP2), CO2, CH4, water vapor and others.

## Slide 18: Instrumentation operational since February 2008
MAAP - Multiangle Absorption Photometer: aerosol absorption at 637 nm
Aethalometer absorption at 7 wavelengths.
TSI Nephelometer: aerosol scattering at 450, 550, 700 nm
CPC 3772: aerosol number concentration
TSI SMPS: aerosol size distribution (10-500 nm)
Stacked filter units: fine and coarse mode aerosol composition – trace elements by XRF and PIXE, BC, ions
Quartz filter for EC/OC analysis (Sunset analyzer)
Ozone monitor (Thermo Environment 42C)
Picarro CO2, CO.
Raymetrics Raman Lidar with 3 wavelengths
AERONET Cimel Sunphotometer and MFR radiometers
Recently ACSM (Aerodyne Aerosol Chemical Speciation Monitor)

## Slide 19
HYSPLIT air mass trajectories wet season 2008

## Slide 20
Chart: Manaus TT34 ZF2 PM10, fine and coarse mode aerosol 2008-2012
Chart: Manaus TT34 ZF2 equivalent black carbon fine and coarse mode aerosol 2008-2012

## Slide 21
Chart: Porto Velho fine and coarse mode aerosol mass 1999-2012
Chart: Porto Velho Black Carbon 2009-2012 Fine and Coarse Mode
Porto Velho aerosol mass concentration and black carbon from 1999 to 2012

## Slide 22
Aerosol particle absorption coefficients at 637nm between February 2008 and May 2011. Statistics were calculated for each 10 Julian days
Particle scattering coefficients at 550nm between February 2008 and May 2011. Statistics were calculated for each 10 Julian days
particle scattering coefficients at 550nm
aerosol absorption coefficients at 637nm
Seasonality of scattering and absorption

## Slide 23
Monthly statistics (2009 – 2012) for light scattering coefficient σs at 637 nm and light absorption coefficient σa at 637 nm in Mm-1 for Porto Velho (PVH, in black) and central Amazonia (TT34, in red).
Single Scattering Albedo Lower at the pristine site
Scattering, absorption and SSA in Manaus and Porto Velho
Artaxo et al., 2013

## Slide 24
Manaus organic aerosol wet season measurements
Brito et al., 2013

## Slide 25
Organic aerosol measurements in Rondonia
Brito et al., 2013

## Slide 26: No new particle formation observed at surface under pristine conditions in Amazon
New particle formation: a two-step process:
1st step: sulfuric acid and amines, ammonia, or organic vapor form stable clusters
2nd step: organic vapor leads to enhance growth rate of the clusters to larger sizes.
Why no new particle formation?
Low SO2 concentration (20-30ppt) suggests the concentration of H2SO4 is low
Organic concentration may be low for the growth of stable clusters.
What is the impact of Manaus plume on NPF?
Kulmala et al., 2013

## Slide 27
Aerosol size distributions measured in 2009 Apr 4th. There was a burst of ultrafine particles from 2:00 to 4:00 UTC time.
New particle formation? Bursts of particles 10<Dp<30 nm.
New particle formation and subsequent growth was seldom observed along two years of measurements. Nevertheless, in 70% of the days, bursts of particles with diameters in the range 10-40nm were detected. The events usually lasted from 20 to 120min, and the subsequent growth to larger sizes was not always clearly observed.

## Slide 28
Biogenic potassium salt particles as seeds for secondary organic aerosol in the Amazon
Our findings suggest that the primary emission of biogenic salt particles effectively regulates the number concentration of cloud condensation nuclei, directly influencing the microphysics and dynamics of cloud formation and precipitation over the rainforest.
STXM-NEXAFS measurements (Pöhlker et al., 2012)

## Slide 29
Large scale aerosol distribution in Amazonia
Severe health effects on the Amazonian population (about 20 million people)
Climatic effects, with strong effects on cloud physics and radiation balance.
Changes in carbon uptake and ecosystem functioning

## Slide 30: SAMBBA - South American Biomass Burning Analysis

## Slide 31
Flight tracks of the BARCA aircraft campaigns (red: BARCA-A, black: BARCA-B.
BARCA – Balanço Regional de Carbono na Amazonia
USP – INPE - Harvard – Max Plank

## Slide 32
Comparisons of median vertical profiles for the Equatorial Transect east of Manaus (“E. Region”), N and S transects along
60Wlongitude, and near Manaus (excluding local pollution). Note the strong similarities between ABLE-2B and BARCA-B data taken
more than 20 years apart. (Source of ABLE data: Harriss et al., 1990b).
Vertical profiles of CO mixing ratios (A) and CN number concentrations (B) during BARCA-A (excluding the smoky region) and BARCA-B.
Andreae et al., 2012

## Slide 33
Growing Mature Dissipating
Hail
Rosenfeld D., et al., 2008: Flood or Drought: How Do Aerosols Affect Precipitation? Science, 321

## Slide 34
Cloud top pressure (P) vs. AOD
Clouds and aerosols in Amazonia
Koren et al., Science 2008
Microphysics
absorption effects
Cloud fraction vs. AOD.

## Slide 35
(a) Correlation coefficient between AOD and precipitation for September 1995–2007. (b) Correlation p value.
Correlation between aerosols and precipitation in Amazonia
Region-mean end of dry season and corresponding 550-nm AOD.
Aerosols extending the duration of dry season
Bevan et al., JGR 2009

## Slide 36
Dust relation to ice-nucleus measurements. Dust concentrations during AMAZE-08. a, GEOS-Chem simulated dust from 2–6 March at 18 UTC. The field site, shown as a black diamond, typically fell near the edge of the plumes. Fine-dust concentrations from PIXE measurements (black rectangles; µg/m³, dp<2µm.
Ice nuclei from biogenic emissions and Sahara dust in Central Amazonia

## Slide 37
Rain rate (TRMM) versus Aerosol Optical Depth (MODIS)
13:30 local-time map of rain rate (R) and the observed trend with aerosol loading in four selected regions. Period: July and August 2007. b, The average R values are plotted for six aerosol-loading sets (blue, including zero R grid squares; red, without zero R grid squares). Note the R intensification as a function of AOD in all cases. (Koren et al., Nature 2012)
Amazonia

## Slide 38
Maximum monthly, annual mean and minimum monthly mean Amazon river discharge at Óbidos and in green maximum and minimum daily mean river discharge, (b) δ18O in precipitation in Bolivia derived from tree rings (Brienen et al. 2012) and (c) tropical Atlantic sea surface temperature from Extended reconstructed sea surface temperature) (Gloor et al. 2013).
Is the Amazonian hydrological cycle intensifying?

## Slide 39
Average spatial distribution of the direct radiative forcing (DRF) of biomass burning aerosols in Amazonia during the dry season of 2010
CERES (Clouds and the Earth's Radiant Energy System) and MODIS

## Slide 40
Land-use change radiative forcing. Forested areas are selected in red and deforested areas are selected in yellow.
Mean Diurnal Radiative Forcing due to change in surface albedo in Rondonia:
-7.3 + 0.9 W/m2
Mean Diurnal Aerosol Forcing Efficiency:
Forest: -22.5 + 1.4 W/m2
Cerrado: -16.6 + 1.7 W/m2
Water column difference by 6-10%
Forcing of water vapor column: -0.4 to -1.2 W m-2
Sena et al., 2013

## Slide 41
HOW MUCH CARBON DO PLANTS TAKE FROM THE ATMOSPHERE?
MODIS gross primary productivity (GPP) estimation from NDVI 2000-2010
Notes: HOW MUCH CARBON DO PLANTS TAKE FROM THE ATMOSPHERE? SVS CATALOG 3764
Terra - MODIS
Plant life converts atmospheric carbon dioxide into biomass through photosynthesis, a process called 'fixing'. This is one of the main ways in which carbon dioxide is removed from the atmosphere and is a major part of the carbon cycle. The amount of carbon removed is called the gross primary productivity (GPP), and the change in GPP due to rising global temperatures is very important factor in the response of the Earth to climate change.
Data from the MODIS instrument on NASA's Terra satellite has been recently used to calculate the GPP for the whole world for the last 10 years. This animation shows a time sequence of GPP on land as measured by MODIS during the years 2000 through 2009. Two things to note are the year-long productivity of the tropical regions and the large seasonal productivity in the northern hemisphere. A close look at the animation also reveals major urban areas for which the productivity is negligible.

## Slide 42
Temperature
CO2 Concentration
Photosynthesis
BVOC emissions
Aerosol Concentration
+
+
+
+
+
+?
-
Aerosol Effects on Net Plant Productivity
Kulmala et al., 2004

## Slide 43
Strong aerosol effect on forest photosynthesis diffuse radiation have a large effect on CO2 fluxes
Increase in aerosol loading

## Slide 44
Aerosols effects on NEE – Manaus and Rondonia
f max: ~ 0,80
  NEE (max): ~ -20 µmol/m²s
  AOT: ~ 0,5
Manaus K34 tower
(Glauber Cirino, INPA, 2013)

## Slide 45
Transport of Sahara dust and smoke from Africa to Amazonia

## Slide 46
Sahara dust transport to Amazonia
(Yuval et. al, 2011).
Notes: Perfis verticais de retroespalhamento atenuado noturnos (em km-1sr-1) obtidos através do satélite CALIPSO mostram o transporte de areia do deserto do Saara para a região amazônica. Os eixos de perfil de vertical mostram até 5km de altitude ( Yuval et. al, in press).

## Slide 47
Smoke and dust AOD for the 17 observation cases in 2008 indicating the advection of African aerosol toward Amazonia.
African aerosol in central Amazonia
Baars et al., 2011

## Slide 48
Raman Lidar: aerosols and water vapor up to 13 Km in Manaus
Henrique Barbosa, 2011

## Slide 49
- Efeitos diretos sobre o sistema respiratório e cardiovascular
(diâmetros em micrômetros)
Areia fina de praia
Cabelo humano
Combustão de partículas, compostos orgânicos, etc
Poeira, pólen, etc
Brônquios
Bronquíolos
Bronquíolos
respiratórios
Alvéolos
Efeitos do material particulado na saúde da população
Tempo de residência das partículas (Tr)
(Moda fina > Moda grossa)
Populações mais afetadas: crianças e idosos
Fonte: Valdir Soares, 2013

## Slide 50
- Polycyclic Aromatic Hydrocarbons in intense and moderate biomass burning in the Amazon region
53% of identified PAHs are mutagenics
20% of identified PAHs are mutagenics and carcinogenics
Chart: PAHs concentration (ng m-3)
| FLU | FEN | ANT | FLUO | PI | RET | BaA | CRI | BbF | BkF | BeP | BaP | InP | DBA | Bper
Intense Biomass Burning | 0.10222 | 0.27885 | 0.44026 | 0.02508 | 0.24077 | 0.63421 | 0.25157 | 0.2435 | 0.14182 | 0.14901 | 0.28026 | 0.21338 | 0.22416 | 0.30865 | 0.15421
Moderate Biomass Burning | 0.064994 | 0.11009 | 0.096198 | 0.015836 | 0.066493 | 0.1948 | 0.068553 | 0.0633 | 0.036123 | 0.028407 | 0.048156 | 0.044131 | 0.070655 | 0.11766 | 0.054839
Nilmara Alves et al., 2013

## Slide 51
Human lung cells
DNA damage
Cell death
INCREASE THE LUNG CANCER RISK
Mechanisms of action of PM10 in lung cells
Alves, Hacon et al., 2013

## Slide 52
ATTO Footprint
C. Gerbig MPIBGC
Amazonian Tall Tower Observatory ATTO – 320 meters
Long term broad objectives observatory

## Slide 53
ATTO site: Picture of the 85 meters tall tower at the left that is being used for aerosol and trace measurements and the proposed 320 tall tower under construction.

## Slide 54
Experimento GoAmazon 2014

## Slide 55
A expansão da agricultura e a variabilidade climática são agentes importantes nas alterações que estão ocorrendo no ecossistema amazônico. Em partes da região é possível observar sinais de transição para um regime dominado pelas alterações ambientais. Estes sinais incluem mudanças no balanço de energia e hidrológico na porção sul e este da Bacia Amazônica.
Interações entre mudanças globais, mudanças de uso do solo, queimadas, hidrologia, ecologia e dimensões humanas na Amazônia
Forçantes são indicadas por ovais vermelhos. Processos são as caixas verdes e consequencias estão nas caixas azuis.

## Slide 56
Obrigado pela atenção!!!
Processos físicos, químicos, biológicos e sociais na Amazônia forman um sistema fortemente acoplado.
Ainda temos muito a prender como funciona este sistema…